## Slide 1
JioMausam
Q&A BACKUP · PROOF HIERARCHY
What’s proven, what we checked, what isn’t
PROVEN · PUBLISHED
Physics: rain weakens microwave signals (ITU-R P.838)
Method: rain from a phone network (Science 2006)
Scale: country-wide rain maps (PNAS 2013)
Open-source tools exist (pycomlink, KIT Germany)
OUR CHECK · PUBLIC DATA
500 real links, Germany, 11 days, radar as reference
0.95 network-wide match, unseen days
0.88 typical single link
68% of trigger events caught; 18% of our triggers unconfirmed
Rain / no-rain days: 91% detected, 5% false
NOT YET PROVEN · THE PILOT
Jio’s usable coverage → Gate 1
Accuracy in Indian monsoon → Gate 2
Business value inside Reliance → Gate 3
Who pays → payer test in the pilot
Insurance-grade triggers → accuracy + actuarial gates, shadow payouts
We know what is proven. We know what isn’t. The pilot is built around the unknowns.
Our check: our pipeline on the open pycomlink example dataset (KIT, BSD licence), German DWD radar as reference; tuned 10–12 May 2018, scored 13–20 May. Not Jio data.

## Slide 2
JioMausam
Q&A BACKUP · DEFENCE WALL
Every limit we know of, and our answer
Limitation | Our answer
Jio may not have enough usable microwave links | Coverage audit is Gate 1; radar, gauges and satellite still work without links
Fibre doesn’t sense rain | We only use microwave links
A link measures path-averaged rain, not a point | Fusion with radar and gauges turns it into grid estimates
Links alone caught only 68% of trigger events | We never use links alone; accuracy picks the mix
18% of our triggers weren’t confirmed by radar | Multi-source confirmation and local calibration
Rain can be confused with equipment faults | Network telemetry, fault flags and cross-link checks
Performance in India is unknown | Back-test Jio’s archived Mumbai monsoon data (Gate 2)
1 km resolution isn’t guaranteed | Resolution depends on link density and fusion; reported per area
Platforms’ willingness to pay is unknown | Prove value inside Reliance first (Gate 3), then sell
Insurance basis risk | Small zones, multi-source trigger, review process
₹300 payout is arbitrary today | Prototype assumption; set by actuarial calibration
₹208 isn’t priced on the 10 mm in 3 h trigger | Priced on 25 years of daily IMD risk; the pilot recalibrates the trigger
Towers don’t sense heat | IMD stations and satellite feed the same engine
Insurance may never launch | The intelligence business stands on its own