## Slide 1: A weather-decision problem, and a signal Jio may already carry
1 · THE PROBLEM AND THE INSIGHT
SAME CITY, DIFFERENT WEATHER
Rainfall (mm) · 26 July 2005 · IMD
Chart: 
| Santacruz | Colaba
Rainfall (mm) | 944 | 73
WHAT A CITY-LEVEL ALERT SAYS
“Heavy rain in Mumbai.”
WHAT IT NEEDS TO DECIDE
“Which zones do I act on, right now?”
Stations ~20 km apart. In 2020–24, on 5 of 15 heavy-rain days the other station got less than half.
Businesses decide blind
dispatch, incentives, delivery promises
Workers carry the loss
income and safety, street by street
India doesn’t have a weather-data problem.
It has a weather-decision problem.
THE INSIGHT: JIO’S MICROWAVE LINKS MAY CARRY A WEATHER SIGNAL
microwave link between two sites
Rain weakens the signal. Measure the excess loss and estimate path-averaged rainfall along each link, in near-real-time.
Microwave links: usable
Fibre: no rain signal
JIOMAUSAM IS
decision infrastructure, not a weather map
Link signals + IMD radar + rain gauges
Spatial weather grid
Decision-ready alerts and triggers
IT IS
Weather intelligence from existing infrastructure
Alerts and data for businesses
A trigger for future worker protection
IT ISN’T
A new sensor network
A consumer weather app
An insurer, or heat sensing from towers
Rainfall: India Meteorological Department records (26 July 2005); Santacruz vs Colaba daily station reports 2020–24 (NOAA GSOD archive of IMD reports).
Notes: [0:00–0:38] Imagine you’re running deliveries in Mumbai. Your dashboard says: “Heavy rain in Mumbai.” Do you stop the whole city? On 26 July 2005, Santacruz got 944 millimetres of rain. Colaba, 20 kilometres away, got 73. The problem isn’t weather data. It’s knowing what to do, zone by zone. But Jio may already own infrastructure that can carry a signal about that rain. Rain weakens microwave signals between telecom sites. Measure the extra loss and you can estimate rain along each link. JioMausam combines that with radar and gauges into alerts businesses can act on.

## Slide 2: Links alone fall short of our bar, so accuracy decides the mix
2 · WHAT WE CHECKED, AND HOW WE FIX THE LIMIT
PROVEN · PUBLISHED Physics: rain weakens microwave signals. Method: Science 2006, PNAS 2013 (country-wide maps).
OUR CHECK · PUBLIC DATA We ran the open-source method on 500 real links (Germany), radar as reference. Not Jio data.
NOT YET PROVEN · THE PILOT Jio’s coverage, Indian accuracy, business value, who pays, insurance-grade triggers.
68%
of rain events caught by links alone
1,120 of 1,639 radar events · 8 unseen test days
links alone: 68%
our bar: 80%
Event = 10 mm+ of rain in 3 hours in a ~4 km zone. Below our bar, so we never use links alone.
Chart: Network average, hourly (mm/h): links tracked radar closely
CANDIDATE SOURCES AND WHO PROVIDES THEM
Jio microwave links
Jio-owned
Network health: faults, outages, maintenance
Jio-owned
Doppler radar: spatial check
IMD (govt)
Rain gauges: ground truth
IMD · BMC
Satellite: coverage fallback
External
New gauges on Jio sites, only where links are thin
New install
Commercial data, only if it lifts accuracy
Commercial
THE PILOT SCORES EVERY MIX AGAINST HELD-OUT RAIN GAUGES
Links only
our check: 68%
Links + radar + gauges
measured in the pilot
Radar + gauges, no links
shows what Jio adds
Rule: the lowest-cost mix that clears every gate: ≥80% of trigger events · totals within ±10% · under 15% unconfirmed
Messer et al., Science 2006 · Overeem et al., PNAS 2013 · Our check: public pycomlink dataset (KIT), 10–20 May 2018, German Weather Service radar as reference. Not Jio data.
Notes: [0:38–1:13] The physics is well established, so we tested it ourselves: 500 real links from a public dataset in Germany, not Jio’s. The links tracked radar closely, but alone they caught only 68% of rain events. Our bar is 80%. That gap told us how to build JioMausam. So we don’t bet on one sensor. Accuracy decides the mix: Jio’s links, network-health data to filter out faults, radar, gauges, satellite. The pilot tests every combination against held-out gauges. The answer isn’t “Jio only”. It’s the cheapest mix that works.

## Slide 3: Prove it inside Reliance, then sell the same intelligence
3 · BUSINESS MODEL
1 · FIRST PROVING GROUND: RELIANCE
THE HERO TEST
Jio network operations
Can we tell rain-related signal loss from equipment faults before sending a crew?
Potentially fewer wasted visits and earlier flood alerts
Jio owns the network data and controls the decision
Tests accuracy and savings
JioMart and Reliance Retail
Rain-aware dispatch, delivery promises, zone pauses
Tests commercial value
MyJio
Street-level rain alerts for users
Tests reach at scale
Every internal use is a hypothesis the pilot tests.
2 · THEN SELL THE SAME INTELLIGENCE
Rain hits Zone A
JioMausam sends a zone alert + rain estimate
The customer decides: reroute, update ETAs, adjust incentives
Lower disruption
WHO BUYS, AND WHAT
1
Delivery and quick commerce
Alerts
2
Logistics, cities, insurers
Alerts + data
3
Agriculture, power, retail
Data + alerts
We sell: zone alerts · a live rain feed (API) · auditable rain records · trigger data for insurers. Not a weather map.
3 · WHY JIO: INTEGRATION, NOT THE SENSOR
SENSE
Jio network
UNDERSTAND
JioMausam
REACH
Reliance ecosystem
PROTECT
JFS + licensed insurers (optional)
HOW JIO CREATES VALUE
01
Intelligence fees External: API, alerts and data
02
Savings inside Reliance Internal: network ops, delivery, retail
03
Distribution fees Optional: only if Kavach launches
The business stands even if insurance never launches.
Company names are examples of potential buyers, not customers we have spoken to. Jio sells intelligence; each customer owns its decisions.
Notes: [1:13–2:02] Before selling to Swiggy, where do we prove it? Inside Reliance, starting with Jio. A signal drops: is it rain, or is something broken? If JioMausam can answer that before a crew goes out, that’s real value. Then JioMart tests commercial value; MyJio tests reach. Once that works, the same intelligence goes outside. Rain hits Zone A. JioMausam flags it. The platform decides whether to reroute, delay or raise incentives. That’s the product: not a prettier weather map, but a signal that changes a business decision. So why Jio? Not because it invented the physics. The edge is integration: Jio’s signal, JioMausam’s intelligence, Reliance’s proving ground and reach. We can monetise the intelligence outside and create savings inside Reliance, even if insurance never launches.

## Slide 4: Insurance comes last. Test the rest in 90 days
4 · KAVACH, PRICING AND THE ASK
WHERE WE STARTED: MAUSAM KAVACH, ONE APPLICATION, NOT THE ANCHOR
Weather event in a zone
JioMausam supplies trigger data
A licensed insurer would underwrite and pay
Fixed benefit, e.g. ₹300 (prototype)
Why optional: only after the accuracy and actuarial gates (shadow payouts until then) · who pays is still unproven · the insurer carries the risk, never Jio · if it fails, nothing breaks. Eligible = already active in the zone before the event began.
IF WE OFFER IT, WEATHER RISK SETS THE STARTING PRICE
City · product | Trigger | Days a year | Paid days | ₹ a month
Mumbai · Basic | ≥204.5 mm rain a day | 1.1 | 1.1 | ₹45
Nagpur · Basic | ≥47°C | 2.2 | ~1.2 | ₹52
Ahmedabad · Basic | ≥47°C | 0.7 | ~0.6 | ₹29 (min)
Mumbai · Plus | ≥64.5 mm rain a day | 11.9 | 5 (cap) | ₹208
Price = expected paid days × ₹300 ÷ 60% ÷ 12
25 years of IMD records (2000–24). ₹300 and 60% are prototype assumptions; final pricing after actuarial validation. One flat price can’t fit India’s risks.
THE ASK: THREE GATES IN 90 DAYS
DAYS 1–30
Coverage
Audit Jio’s microwave links and data readiness; the audit picks the live city
Gate 1: enough usable coverage?
DAYS 15–60
Accuracy
Back-test archived Mumbai monsoon data against held-out IMD and BMC gauges
Gate 2: does the fused system clear every gate?
DAYS 61–90
Value
Live shadow test in one Reliance operation, matched zones with vs without
Gate 3: does it improve a real operation?
Only after all three gates pass do we scale externally. If not, we stop.
 | 0–3 months | 4–12 months | Year 2 | Year 3
Intelligence | Three gates | Reliance live + first clients | Cities + enterprises | National weather API
Kavach (optional) | Shadow payouts | Sandbox + heat | Basic at recharge | National scale
We aren’t asking Jio to build another weather network, just to discover what its existing one can tell us.
First prove the signal. Then sell the intelligence. Protection comes last.
IMD station data 2000–2024 (NOAA GSOD) · 5-day annual cap · Gate 3 KPIs: site visits, fault-resolution time, delivery delays, rider availability, incentive spend.
Notes: [2:02–2:58] Kavach is where we started: protection for workers. Then we stress-tested it. Who pays? Is the trigger accurate? Can an insurer price it? The insurance isn’t the business; the intelligence underneath it is. So Kavach becomes one application, only after the accuracy and actuarial gates pass. If we offer it, weather risk sets the starting price. From 25 years of IMD records: about 45 rupees a month in Mumbai, 52 in Nagpur, 29 in Ahmedabad, and 208 for Mumbai Plus. All illustrative until actuarial validation. We’re not asking you to believe us. We’re asking Jio to test it. Ninety days, three questions. Does Jio have the coverage? Does the combined system clear our bar? Does it improve a real Reliance operation? If yes, scale. If not, stop. First prove the signal. Then sell the intelligence. Protection comes last.