## Slide 1
JioMausam
Q&A BACKUP · PROOF HIERARCHY
What’s proven, what we checked, what isn’t
PROVEN · PUBLISHED
Physics: rain weakens microwave signals (ITU-R P.838)
Method: rain from a phone network (Science 2006)
Scale: country-wide rain maps (PNAS 2013)
Open-source tools exist (pycomlink, KIT Germany)
OUR CHECK · PUBLIC DATA
500 real links, Germany, 11 days, radar as reference
0.95 network-wide match; 0.88 typical link; 0.78 map level
Rain / no-rain days: 91% detected, 5% false
Links alone failed all three accuracy gates: 68% of trigger events (≥80%), totals 18% low (±10%), 18% unconfirmed (<15%)
NOT YET PROVEN · THE PILOT
Jio’s usable coverage → Gate 1
Accuracy in Indian monsoon → Gate 2
Business value inside Reliance → Gate 3
Who pays → payer test in the pilot
Insurance-grade triggers → accuracy + actuarial gates, shadow payouts
We know what is proven. We know what isn’t. The pilot is built around the unknowns.
Our check: our pipeline on the open pycomlink example dataset (KIT, BSD licence), German DWD radar as reference; tuned 10–12 May 2018, scored 13–20 May. Not Jio data.

## Slide 2
JioMausam
Q&A BACKUP · DEFENCE WALL
Every limit we know of, and our answer
Limitation | Our answer
Jio may not have enough usable microwave links | Coverage audit is Gate 1; radar, gauges and satellite still work without links
Fibre doesn’t sense rain | We only use microwave links
A link measures path-averaged rain, not a point | Fusion with radar and gauges turns it into grid estimates
Links alone failed all three accuracy gates | We never use links alone; accuracy picks the mix
18% of our triggers weren’t confirmed by radar | Multi-source confirmation and local calibration
Rain can be confused with equipment faults | Network-health flags (faults, outages, maintenance) and cross-link checks
Performance in India is unknown | Back-test Jio’s archived Mumbai monsoon data (Gate 2)
1 km resolution isn’t guaranteed | Resolution depends on link density and fusion; reported per area
Platforms’ willingness to pay is unknown | Prove value inside Reliance first (Gate 3, matched zones), then sell
Insurance basis risk | Small zones, multi-source trigger, review process
₹300 payout is arbitrary today | Prototype assumption; set by actuarial calibration
₹208 isn’t priced on the 10 mm in 3 h trigger | Priced on 25 years of daily IMD risk; the pilot recalibrates the trigger
Towers don’t sense heat | IMD stations and satellite feed the same engine
Insurance may never launch | The intelligence business stands on its own

## Slide 3
JioMausam
Q&A BACKUP · TOUGH QUESTIONS
The questions we expect, and short answers
If a judge asks | Say
“Your correlation is 0.95. Why only 68%?” | 0.95 is the network-wide hourly match, where local errors cancel. At map level it’s 0.78, and a trigger test is harsher: 9 mm against an 11 mm trigger is a miss. Links also read 18% low.
“Mumbai already has hyperlocal weather.” | Exactly: BMC gauges and IMD radar are inputs we fuse, not rivals. The pilot’s “radar + gauges, no links” run measures what Jio’s links add.
“Jio already knows rain fade.” | It may. Then Gate 1 confirms cheaply what weather information is available. If it doesn’t, the same telemetry is a new signal.
“What if it doesn’t rain in days 61–90?” | The back-test replays archived monsoon events, including network-ops value. The full live test runs in Mumbai’s 2027 monsoon (months 4–12).
“Why ₹208 if the live trigger is 10 mm in 3 h?” | ₹208 isn’t priced from that prototype trigger. It uses 25 years of daily IMD heavy-rain history, capped at five paid days. The pilot measures the 3-hour trigger’s real frequency and recalibrates before launch.
“Did you build the model?” | We didn’t invent the method; it’s published research. We implemented it with open-source tools, ran it ourselves on real link data, and measured where it fails.
“Germany isn’t India.” | Agreed. Gate 2 back-tests Jio’s archived Mumbai monsoon data against held-out IMD and BMC gauges. Nothing scales until it passes.
“Who decides whether Jio’s own system pays?” | Jio only supplies the trigger data. A licensed insurer owns the contract, the rules and the payout; the trigger is multi-source and auditable.